## Slide 1
TEAM:
Affan Pathan
L Shreya
Prathamesh Nerpagar
OLYMPUS TECH 2.0 - CUBESAT

## Slide 2
Designing Conditions
2. Temperature variations of 180-300K.
  Orbiting venus near exosphere
3. Presence of high amount of solar radiation against satellite
4. Acidic corrosive atmosphere
5. 30 days life expectancy of the satellite

## Slide 3
Satellite Constraints
  The satellite is designed for orbiting a polar orbit around the planet such that it doesnt go into shadow for long periods
2. The weight of satellite is 1.48Kg
3. Theres a presence of a larger satellite serving as relay for communication from earth.
Due to weight and power constraints, we cannot fit a long range communication system in the satellite itself.

## Slide 4
Design
  Satelllite features an always sun facing heat shield.
The heat shield is coated with highly refletive coating to reflect back maximum possible radiation in space
  Two lateral sides of satellite feature solar panels, which are retractable with help of two actuators.
The solar panel also has an infrared radiator which rejects heat to the shadow side
  The planet facing side of the satellite has a flap cover for payload, exposing an array of sensors and cameras to assess the planet
  The solar panels on opening expose the sensor array to the surface of the planet

## Slide 5
DESIGN SKETCH:

## Slide 7
Censors and Data Collection
  Standard High-Res imager for surface photos
  Thermal imager for analysing winds
  UV and IR spectrometers for analysing the gases in atmosphere
  Magnato-meter for analysing magnetic field
  All electronics will be radiation hardened

## Slide 8
Materials
  Body mad of carbon fibre
-> lightweight
-> 1.6gm/cm3
2. Heat shield made of aluminium, coated with highly reflective materials
->2.7gm/cm3
3. High density Li-CFx battery
-> Not rechargable, but packs punch
->100gm battery ; 200W/Hr
-> Bears high temps till 400C
4. Gold foil coating for exterior

## Slide 9
Weights
  Solar panels : 350gm ; 15-20W/Hr
2. Heat shield : (15*15*1)cm *2.7gm/cm3 = 607.5gm
3. Battery packs : 100gm Li-CFx
4. Electronics and sensors : 125gm
5. Body:
6*(15cm long+0.5cm diameter)
3*(15*15*0.25)
panels = 168.75cm3
total weight = 185.75*1.6gm/cm3 = 297gm
TOTAL WEIGHT : 1.48Kg

## Slide 10
Issues
  The weight is 1.5Kg, while 1Kg was expected. This is due to requirment for heat proofing equipment
2. Requirement for relay of comms the satellite. Cannot send signals directly to earth, needs a relay near venus
Refernces
  Li-CFx Battery : https://pubs.rsc.org/en/content/articlelanding/2023/ee/d2ee04179k
2. Radiation shielding :

## Slide 11
QUESTIONS?